## Slide 1: AutoCalib: Automatic Traffic Camera Calibration at Scale
microsoft reaserch: Romil Bhardwaj, Ganesan Ramalingam, Ramachandran Ramjee
ohio state univeersity: Gopi Krishna Tummala, Prasun Sinha
Proceedings of the 4th ACM International Conference on Systems for Energy-Efficient Built Environments (BuildSys 2017), Delft, The Netherlands, November 2017.
Presented by tengxiang wang

## Slide 2: Traffic cameras: what they can do
Identifying speeding vehicles, city road planning, accident prediction and prevention, etc.

## Slide 3: Traffic Camera calibration
Camera Parameters:
  Intrinsic Parameters:
    Focal length
  Extrinsic Parameters:
    Orientation (rotation matrix R),
    Position of the camera in real-world coordinates(T)
Challenges: requires enormous manual effort

## Slide 4: Calibration problem
R: rotation matrix
T: translation matrix
Perspective-N-Point problem:
  With n ≥ 4 different points, as well as the camera’s intrinsic parameters, we can solve for the camera’s extrinsic parameters using equation 1.
  Call solution SolvePnP

## Slide 5: Current calibration works

## Slide 6: aUTOCALIB System Design
Challenges:
  Low-resolution images, error in vehicle detection and classification.
  Detecting and annotating key-points: Point of interest: tail lamps, side mirrors, etc.
  Consolidating a set of calibrations
Vehicle Detection
Automatic Key-point Annotation
Vehicle Model-based Calibration
Filtering and Averaging Calibrations

## Slide 7: aUTOCALIB PIPELINE

## Slide 8: aUTOMATIC KEY-POINT ANNOTATION
CompCars DNN for transfer learning to reduce trainning data and time
Manually annotated 486 images for trainning

## Slide 9: Vehicle model-based calibration
Real-world 3D coordinates of the key-points
With SolvePnP to calibrate the camera
10 car models selected.
Low resolution image is a disaster for car classification
Every identified car image producing 10 calibrations!

## Slide 10: Filtering and averaging calibrations
Large # of calibrations
Annotation errors: DNN-based annotation tool introduces an error of a few pixels
Vehicle identification errors: The car in the image may not belong to any of the 10 models.
Statistical filters

## Slide 11: Evaluation
Key-point annotation accuracy

## Slide 12: Evaluation
Ground truth for evaluation:
  Example of Ground Truth Keypoints (GTKPs) marked in a frame.
The distance measurement errors for the ground truth calibrations, which are indicative of the errors in GTKP annotation, have an average RMS error of 4.62% across all cameras. AutoCalib has an average error of 8.98%.

## Slide 13: Calibration accuracy

## Slide 14: Calibration accuracy

## Slide 15: A comparison to related works
Vanishing Point-based approaches

## Slide 16: Discussion